## Slide 1
THE DELAY
The useful endpoint arrives at DIV12. Triage should not wait blindly.
MEACompass | locked retrospective evidence
01
Rat cortical neural network formation is measured over days—not in a single snapshot.
DIV5
DIV7
FORECAST / WAIT
DIV12
5 days
DIV7 forecasts are available five days before the DIV12 endpoint for accepted cases.
136 chemicals • 4,192 complete longitudinal trajectories

## Slide 2
THE CONCEPT
MEACompass forecasts—and knows when not to.
Evidence, uncertainty, and human review are part of one workflow.
MEACompass | locked retrospective evidence
02
OBSERVED
DIV5 + DIV7 physiology
PREDICTED
DIV12 value + 90% interval
DECISION SUPPORT
accept or abstain
HYPOTHESIS
future neural OoC adaptation
Uncertain cases continue to DIV12. MEACompass never terminates an assay autonomously.

## Slide 3
SCIENTIFIC BOUNDARY
A credible forecast begins with an honest boundary.
MEACompass | locked retrospective evidence
03
WHAT THIS IS
Retrospective rat cortical neural microelectrode-array research
Chemical-disjoint DIV12 prediction
Calibrated research decision support
WHAT THIS IS NOT
Not organ-on-chip training data
Not human or external-device validation
Not an autonomous assay-termination system
Human neural OoC transfer remains a hypothesis until a frozen prospective study validates it.

## Slide 4
EVALUATION DESIGN
The split follows the chemical—not the convenient row.
Every dose, alias, replicate, and well for one chemical stays together.
MEACompass | locked retrospective evidence
04
136 CHEMICALS
Canonical CAS groups
4,200 complete trajectories
3 × 5 OUTER FOLDS
Held-out chemicals only
Inner validation selects baselines and settings
CHEMICAL BOOTSTRAP
Paired uncertainty at the true generalization unit
Outer-test labels evaluate. They never select.

## Slide 5
LOCKED PRIMARY RESULT
Frozen M1 improves all five endpoints against the fair comparator.
MAE gain versus inner-selected BT+; every paired chemical-bootstrap interval excludes zero.
MEACompass | locked retrospective evidence
05
Firing
14.2%
Bursts
17.0%
Active electrodes
39.0%
Network spikes
15.6%
Coordinated activity
22.7%
BT++
12.3–42.9%
gain versus the stricter post-audit comparator; significant on all five endpoints
DIV7 contribution
56.9–77.3%
Chemistry 11.2–31.8% • association, not mechanism
Failure case disclosed: tributyltin chloride

## Slide 6
INTEGRITY BEFORE MOMENTUM
The negative control stopped us—then the audit earned conditional continuation.
MEACompass | locked retrospective evidence
06
REGISTERED STOP
Chemical-block permutation showed a small bursts gain.
BOUNDED AUDIT
No future-derived feature
Clean full-target shuffle
No alignment defect
Real M1 beat all 20 block-null runs
CONDITIONAL PASS
Failure remains visible
BT++ added as safeguard
Locked claims unchanged
The audit resolved a mechanism question. It did not erase the original stop.

## Slide 7
CALIBRATED UNCERTAINTY
Nominal 90% intervals cover 91.0–92.4% in held-out chemicals.
MEACompass | locked retrospective evidence
07
90% nominal
Bursts 91.08%
Firing 91.53%
Active 92.13%
Spikes 91.03%
r 92.40%
Nested group CV+ • calibration uses training chemicals only • intervals travel with every forecast

## Slide 8
SELECTIVE PREDICTION
Abstention clears the risk threshold on three endpoints—not five.
Accepted-case MAE reduction at 70% retained coverage; registered threshold = 15%.
MEACompass | locked retrospective evidence
08
Firing
18.9%
PASS
Bursts
4.6%
LIMITATION
Active electrodes
18.0%
PASS
Network spikes
5.3%
LIMITATION
Coordinated activity
28.4%
PASS
Uncertain cases continue to DIV12; this policy does not terminate assays.

## Slide 9
TIME CAUSALITY
DIV7 is the earliest useful decision point; interpretability explains why.
MEACompass | locked retrospective evidence
09
DIV5
weaker
DIV5 + DIV7
primary locked model
DIV5 + 7 + 9
post-lock ablation
DIV12
observed endpoint
DIV7
56.9–77.3%
CHEM
11.2–31.8%
One disclosed failure: tributyltin chloride
Interpretability is predictive, not causal.

## Slide 10
WORKING INTERFACE
The demo keeps evidence, forecast, and hypothesis visibly separate.
MEACompass | locked retrospective evidence
10
REAL DEMO CAPTURE REQUIRED
The local static demo is complete, but the mandated in-app browser connection was unavailable in this session. No fake screenshot has been substituted.
docs/demo/index.html • precomputed held-out predictions • no external requests

## Slide 11
ADAPT, DO NOT DEPLOY BLINDLY
Cohort-shift evidence is encouraging; a new chip still requires local validation.
MEACompass | locked retrospective evidence
11
POST-LOCK SECONDARY
5 / 5
endpoint wins in both directions
ToxCast → NTP
10.3–34.5%
NTP → ToxCast
15.1–50.3%
Held-out cohort shift; not external laboratory/device transfer.
1 MAP
Local endpoints + controls
2 RETRAIN
Local longitudinal data
3 RECALIBRATE
Intervals + drift
4 VALIDATE
Prospective human review
The frozen EPA model is not a deployable neural OoC model.

## Slide 12
REPRODUCE WITHOUT RETRAINING
The locked evidence rebuilds in minutes from committed predictions.
MEACompass | locked retrospective evidence
12
$ make setup
$ make fetch-results
$ make test
$ make reproduce-lite
$ make demo
NO AUTOMATIC RETRAINING
Saved predictions → tables → figures → demo
Manifest hashes verify the evidence bundle.
Full training requires an explicit locked-rebuild flag.
Forecast when evidence is strong; continue the assay when it is not.