## Slide 1
N E U R O C H I P - T W I N
Locked retrospective result • EPA rat cortical neural MEA
01
FORECAST
five days earlier
—with permission to wait.
DIV7 → calibrated DIV12 forecast for unseen chemicals
DIV5
DIV7
DIV12
OBSERVE
PREDICT / ABSTAIN
VERIFY
14.2–39.0%
MAE GAIN VS BT+
all 5 endpoints significant
91.0–92.4%
INTERVAL COVERAGE
nominal 90%
3 / 5
ABSTENTION ENDPOINTS
clear 15% risk threshold
5 days
EARLIER FOR ACCEPTED CASES
research decision support

## Slide 2
S C I E N T I F I C B O U N D A R Y
docs/neurochip_data_audit.md
02
The boundary makes the result credible.
WHAT THIS IS
Rat cortical neural
microelectrode-array assay
Longitudinal electrophysiology across DIV5, DIV7, DIV9, and DIV12.
WHAT THIS IS NOT
Not organ-on-chip data.
Not human validation.
No autonomous assay termination. Prospective transfer remains the next experiment.
136
CANONICAL CHEMICALS
4,192
COMPLETE TRAJECTORIES
99
PLATES / BATCHES
2
COHORTS

## Slide 3
E V A L U A T I O N A R C H I T E C T U R E
3 seeds × 5 outer folds • inner selection only
03
Chemical identity never crosses the outer split.
01
CANONICALIZE
CAS RN groups aliases, doses, wells, and replicates.
02
OUTER GROUP SPLIT
Unseen chemicals only in the held-out test fold.
03
INNER GROUP CV
Choose baseline and hyperparameters without test labels.
04
ONE-SHOT TEST
Predict DIV12; estimate uncertainty; never tune back.
ALLOWED
DIV5 + DIV7 physiology • dose • cohort • structure
FORBIDDEN
DIV9/DIV12 features • potency • hit calls

## Slide 4
H E L D - O U T P E R F O R M A N C E
results/gate_s_main.csv • chemical-level paired bootstrap
04
M1 beats the fair comparator on all five endpoints.
ACTIVE ELECTRODES
39.0%
95% CI below 0
COORDINATED ACTIVITY
22.7%
95% CI below 0
BURSTS / MIN
17.0%
95% CI below 0
NETWORK SPIKES
15.6%
95% CI below 0
FIRING RATE
14.2%
95% CI below 0
0
10
20
30
40
RELATIVE MAE GAIN VS INNER-SELECTED BT+
BT++ • 12.3–42.9%

## Slide 5
I N T E G R I T Y B E F O R E N O V E L T Y
results/gate_s_decision.json • results/audit/
05
A failed negative control stopped the pipeline.
REGISTERED STOP
Permutation retained a small burst gain
ΔMAE −0.525
CI [−0.969, −0.136]
BOUNDED AUDIT
Feature lineage • alignment • full shuffle • 20 block-null runs
No leakage found
Full shuffle clean
CONDITIONAL CONTINUATION
Real M1 exceeds every null run on all five endpoints
BT++ required
Original STOP retained
The audit explains the null structure; it does not erase the registered failure.

## Slide 6
C A L I B R A T I O N
results/m2_calibration.csv • nested group CV+
06
Nominal 90% intervals cover 91.0–92.4%.
90% nominal
BURSTS / MIN
91.08%
FIRING RATE
91.53%
ACTIVE ELECTRODES
92.13%
NETWORK SPIKES
91.03%
COORDINATED ACTIVITY
92.40%
89%
90%
91%
92%
93%
90.36%
minimum cohort coverage
No CQR switch needed

## Slide 7
S E L E C T I V E P R E D I C T I O N
results/m3_risk_coverage.csv • 70% retained coverage
07
Abstention helps three endpoints—not five.
15% GATE
COORDINATED ACTIVITY
28.4%
PASS
FIRING RATE
18.9%
PASS
ACTIVE ELECTRODES
18.0%
PASS
NETWORK SPIKES
5.3%
LIMITATION
BURSTS / MIN
4.6%
LIMITATION
Widest 30% of intervals → CONTINUE TO DIV12

## Slide 8
T I M E A B L A T I O N
results/time_ablation.csv • DIV9 is post-lock only
08
DIV7 is the useful decision point.
ENDPOINT
DIV5
DIV5 + 7
DIV5 + 7 + 9
BURSTS / MIN
32.39
27.17
23.58
FIRING RATE
46.36
39.29
34.41
ACTIVE ELECTRODES
27.66
20.42
16.67
NETWORK SPIKES
45.78
40.72
37.28
COORDINATED ACTIVITY
58.83
48.61
48.74
5 DAYS
earlier per accepted forecast
41.7%
of stated 12-day duration
No monetary claim

## Slide 9
I N T E R P R E T A B I L I T Y
results/feature_importance.csv • exact tree contributions
09
Physiology leads; chemistry adds context.
DIV7 PHYSIOLOGY
56.9–77.3%
CHEMISTRY
11.2–31.8%
DIV5 PHYSIOLOGY
3.7–17.6%
Predictive contribution ≠ causal mechanism
SHOW FAILURES
Tributyltin
chloride
Mercuric
chloride
Case selection disclosed after lock
M1 significantly beats B3 on 2 / 5 endpoints—not all five.

## Slide 10
P R O S P E C T I V E P A T H
Frozen model • prospective validation required
10
The next experiment is human neural OoC validation.
01
FREEZE
Endpoints, criteria, and external test set
02
COLLECT
Devices, labs, batches, and unseen chemicals
03
VERIFY
Error, coverage, abstention, and drift
04
GOVERN
Human review, override, and monitoring
REPRODUCE IN MINUTES
make test • make reproduce-lite • make demo
44 / 44
tests passing
Forecast when evidence is strong. Continue when it is not.